# SINGLE ELECTRIC CONVECTION OVEN SPECIFICATIONS

Single Electric Convection Oven - Shall be Model Zephaire-E-100 Single as manufactured by Blodgett Oven Corporation. Oven shall have all standard features of Zephaire E 100 series ovens and the following:

  - Solid state manual temperature controllers.

  - Stainless steel front, top, and sides.

  - Glass doors.

  - Standard depth oven

  - 25" legs.

  - 2-speed, fan motors.

  - Simultaneous opening doors operated by single heat resistant porcelain handle.

  - 11 KW per section

  - Double sided porcelain enameled steel baking interiors.

  - Electronic spark-to-pilot ignition.

  - Controls mounted on a positive disconnect slide-out module for ease of service.

  - 2 year parts and 1 year labor warranty, 3 year door warranty

  - Performance Check to be performed by Factory Authorized Service Agency.

  - Voltage and phase to be:____________

OPTIONAL ACCESSORIES / MODIFICATIONS

-	Casters

-	S/S back panel (recommended if unit is not against a wall)

-	Extra oven racks

- Solid s/s doors - N/C

BIDDER REQUIREMENTS

- ELIGIBLE BIDDER MUST VISIT JOB SITE.

- ALTERNATES NEED TO BE SUBMITTED FOR APPROVAL 10 DAYS PRIOR TO BID OPENING.

- SUCCESSFUL BIDDER TO DELIVER, UNCRATE, SET IN PLACE, LEVEL, AND REMOVE CRATING.

- FINAL CONNECTIONS BY OTHERS

- BIDDER WILL HONOR PRICES FOR A PERIOD OF ONE YEAR FROM THE BID DATE____YES____NO.

- BIDDER WILL HONOR PRICING FOR COOPERATIVE PRICING____YES____NO.

(Additional travel/mileage charges may apply to systems that are located outside the bidding system’s area)